3670 -A Wheeler Avenue, Alexandria, Virginia 22304

Phone: 703-751-8500 Fax: 703- 751- 8733

www.Leitner-Wise.com

The New Coast Guard Service Rifle

Features: The LW15.499 rifle is a lightweight, air-cooled, gas-operated, magazine-fed, shoulder- or hip-fired weapon designed for either automatic fire, 3-round burst fire or semi-automatic fire (single shot) through the use of a selector lever. The rifle is based on the M16A2 rifle and shares the same features.

The upper receiver/barrel assembly has an integral compensator which helps keep the muzzle down and minimize felt recoil during firing.  The steel bolt group and barrel extension are designed with locking lugs which lock the bolt group to the barrel extension allowing the rifle to have a lightweight aluminum receiver.  The bolt group itself has dual extractor springs preventing spring fatigue.  The rifle and upper receiver come with a one-piece integral rail system at the 12, 3, 6 and 9 o’clock positions extending over the barrel.

Background: The LW15.499 rifle is a product improvement of the M16 series rifles and is designed to address the lack of knock-down power of the 5.56 mm round.  As noted above, the rifle shares the features and controls of the M16 thus minimizing the retraining requirements.  Originally designed in 1994, the rifle fires a purpose designed .499 caliber projectile weighing 300 grains, developing a muzzle velocity of over 2,200 fps and muzzle energy of in excess of 3,000 f/lbs.  Three projectiles are available; training, duty and armor piercing all being frangible and made from a copper/tin alloy.  The rifle is capable of discharging other projectiles based upon end-user requirements.  The rifle is intended as a short range (500 meters) anti-personnel/anti-material infantry weapon and displays terminal ballistics similar to the .50 BMG round at up to 200 meters.

An additional advantage of the rifle is that the upper receiver, bolt carrier group and barrel assembly can be mated to any mil spec AR15/M16/M4 lower receiver with no additional modifications, ammunition being fed from a dedicated straight 10 or 12 round magazine.  A 60 round drum magazine is also available for military and LE applications.

Applications

- Can be retrofitted into existing AR15/M4/M16 weapons platforms reducing both acquisition and training costs dramatically

- Retrofitted weapons run at reduced operating stresses, pressures and temperatures

- The .499 ammunition has outstanding ballistic efficiency

- Overwhelming terminal ballistics

- Anti-personnel and anti-material role in one munition

- No over-penetration – Non Lead Frangible Projectiles

- Vehicle stopping applications – Armor Piercing Applications

- Perimeter Defense / Area Denial

- Door / Barricade breaching

# Text boxes

Manufacturer:  Leitner-Wise Rifle Co. Inc.

Overall Length:  36.25 in (920.75 mm)

Weight without Magazine:  6.275 Lb (2.8 Kg)

Empty Magazine (10 RD):  .25 Lb (.11 Kg)

Loaded Magazine:  1.0 Lb (.45 Kg)

Caliber:  0.499 (12.675 mm)

Effective range:  1312.4 feet (400 meters)

Barrel Construction:  Stainless Steel; Alloy Steel

Barrel Length with Integral Compensator:  18 in (457.2 mm)

Rifling Twist:  1 turn in 19"

Method of Operation:  Gas

Muzzle Velocity:  2,200 ft/sec (670.6 m/sec)

Rate of Fire (RPM):  500-940

Type of Fire:  Semi-Automatic/ Full Automatic

3-Shot Burst Option:  Available

Magazine Capacity:  10 RD / 12 RD / 60 RD Drum

Unit Replacement Cost: $1,385.00 Rifle – Chrome molly barrel

$1465.00 Stainless Steel Barrel

$ 895.00 (Upper Receiver & Magazine)