ROBOPAC ROTOPLAT

SEMIAUTOMATIC STRETCH WRAPPER

MODEL 506/PFS

(November 2002)

Rotoplat Model 506 PFS Turntable Style Stretch Wrapping System consisting of:

Standard Features:

Touch sensitive push button control panel with programmable microprocessor with the following functions adjustable from control panel:

Rotation speed (5-12 rpm)

Bottom wrap selector (0-10)

Top wrap selector (0-10)

Film pre-stretch ratio 0-250%)

Sensing delay for photocell

Up/Down standard wrap cycle or Up only cycle

Top sheet cycle

Reinforcing wrapping cycle

Film carriage type “PFS” with powered pre-stretch rollers, adjustable from 0% - 250% via control panel

Film carriage raise speed fixed with 20% overlap ( standard ) Synchronized with table rotation speed

65 Inch diameter variable speed turntable with the following features:

3/8 Inch steel plate with non-slip raised diamond surface

Maximum table rotation speed 12 rpm

Soft start feature with controlled acceleration and deceleration

Fixed point table stopping

16 Heavy Duty support casters under table

4400 Pounds maximum weight capacity

95 Inch maximum wrapping load height (standard)

Photocell for automatic load height sensing

110 Volt standard power supply requirement

PRICE		$ 7,995

ROTOPLAT 506 PFS OPTIONAL CONFIGURATIONS:

Same as above but with 70 inch table	$ 8,695

Model 506PFS (std machine) with built-in

Scale, for Loads up to 5,000 pounds		$13,245

OPTIONS:

Variable raise speed film carriage		$    550

Ramp for 65 inch turntable			$    550

Ramp for 70 inch turntable			$    650

Top hold down, pneumatically operated

for standard 95” mast			$ 1,800

Top hold down, pneumatically operated

for optional 110” mast			$ 1,950

TERMS:

Net 30 days with approved credit

WARRANTY:

3 Year standard warrantee on parts not damaged by misuse or neglect.

LEASING OPTIONS:    Based on List Price of $7,995

10% Purchase Option Lease             $1.00  Purchase Option Lease

Term               Payment                                  Term                Payment

36                  $253.00                                     36                   $270.00

48                  $200.00                                     48                   $214.00

60                  $167.00                                     60                   $176.00

Requires 2 payments in advance.

All payments and terms subject to credit approval.

PRICES AND SPECIFICATIONS ARE SUBJECT TO CHANGE WITHOUT NOTICE