RF Networks

Model 2120 Telemetry Demodulator

FEATURES Agile Data Rates 1 to 20 Mbps Receives SOQPSK, FQPSK†, OQPSK, or QPSK Intermediate Frequency of 70 MHz or 20 MHz Programmable Control, Local and Remote via IEEE-488 Bus Spectral Inversion Control Fault Messaging IRIG-106-00 Compatible APPLICATIONS Telemetry Guidance Satellite Field Training Simulation

# Model 2120 Telemetry Demodulator

The Model 2120 is a high-speed demodulator designed to receive a family of modulation methods including SOQPSK, FQPSK†, OQPSK and QPSK. It will yield low BER with the lowest possible C/N or corresponding Eb/N0 to optimize the range/distance and the quality of the received data. The FQPSK mode provides spectrally efficient point-to-point data reception suitable for operating on links serviced by non-linear amplifiers (such as fully saturated Class C) - without significant spectral restoration. It has been demonstrated to be a suitable replacement for PCM/FM receivers wherever increased data density is required from higher data rates or reduced spectral allocations. The OQPSK mode is today's non-linear solution. The QPSK mode has uses in other applications where linear amplification is the norm. The Model 2120 provides complete data rate flexibility over the 1 to 20 Megabit per second range and cover most requirements. The user is provided with the selection of either 70 MHz or 20 MHz as the intermediate receive frequency, allowing compatibility with currently used down converters. The RF Networks Model 2120 operates without additional IF or RF filters and displays a robust bit error performance without the need for additional coding. The Model 2120 is the third generation of FQPSK receiver from RF Networks.

Model 2120 Telemetry Demodulator

TECHNICAL SPECIFICATIONS

General - RF

| Mode | Receive Only |
| --- | --- |
| Data Rate | 1.0 Mbps to 20 Mbps, in 1Kbps steps, tracking to 1 bps |
| Modulation | SOQPSK, FQPSK†, OQPSK, or QPSK |
| RF Carriers | 70 MHz or 20 MHz, selectable |
| BER | 1 x 10-5 for a C/N of 15 dB and two adjacent like channels of the same amplitude (for FQPSK) |
| IF Impedance | 50 ohms |
| IF Impedance Mismatch | 1.4:1 VSWR all possible angles |
| Input Level | -45 dBm to +10 dBm, AGC Controlled |
| Rate, Carrier Tracking | Up to 50 kHz per second. |
| Range, Carrier Acquisition | Up to ±100 kHz from nominal center frequency |
| Range, Carrier Tracking | Up to ±100 kHz from nominal center frequency |
| Time, Initial Acquisition | 25 ms or less (at 15 Mbps) |
| Threshold Acquisition | 6 dB Eb/N0 |
| Time, Fade Recovery | 5 ms or less (at 15 Mbps) |
| De-randomizer | 15-bit RCC standard, selectable |

Data Output

| DM Output | Replica of NRZL serial data stream applied to Tx |
| --- | --- |
| Intrinsic Clock Jitter, Interface | 5% peak-to-peak |
| Intrinsic Data to Clock Skew | ± 5 %, systematic and jitter |
| Interfaces | TTL and ECL |

Physical

| Power | 90 to 265 volts, 50/60 Hz, autoranging. |
| --- | --- |
| Physical Dimensions | 19" wide by 1-3/4" high by 16" deep, mounting ears included |
| Weight | 7.5 lbs |
| Temperature | 0o to +50o C operating, -20o to +85o C storage |
| Humidity | 5% to 95% non-condensing |
| Altitude | Up to 5000 meters MSL operating, 16000 meters MSL shipping |

Mating Connectors

| RF Receiver Input | BNC connector, 50 ohms unbalanced |
| --- | --- |
| Data Interfaces | TTL - BNC, 50 ohms - data and clock; ECL - DB9, Female D |
| Control Interface | IEEE-488 compliant including protocol (except power) |

†  FQPSK is a Feher patented QPSK licensed from Digcom, Inc.  RF Networks, Inc., is a licensee of FQPSK.

___________________________________________________________________________________________________________

RF Networks, Inc.

10201 N. 21st Avenue, Unit 9  Phoenix, AZ  85021  (   (602) 861-3652  (   FAX: (602) 861-0251

© RF Networks, Inc.  2000    (   Specifications Subject to Change Without Notice