# C3 - C45 and C60  - CARGO HOOKS

The C- series Cargo Hooks were designed for helicopter ”long-line” operations in single installation, and multiple hook carousel configurations.

##### All Hooks available Keeper or Keeperless

- Positive locking toggle mechanism and low voltage opening.

- Safety factor for Ultimate Designed Strength is 4.

- Minimum load for release: 7lb. [3kg]

- Load beam snout is designed for load rings with internal diameter between (2.5 - 4”.

- Adjustable tension load beam return spring.

- High strength Aluminum / steel construction

- 1.4” [35mm] throat opening

- Oversized load beam saddle

*C3 accomodates 6 x ½” ropes

*C45-C60 accommodate 8 x 5/8” ropes

- Electrical and manual release

- Low maintenance / Reduced overhaul costs

- A quick solenoid change option is available – replace the solenoid by removing the solenoid cover only

| Model | Lift Capacity | Weight | Height | Width | O/A Thickness |
| --- | --- | --- | --- | --- | --- |
| C3 | 3,000 lbs [1360 kg] | 5.5lb [ 5kg] | 9” [ 229 mm] | 8.1” [ 206 mm] | 4.3” [102 mm] |
| C45 | 4,500 lbs [2000 kg] | 15lb [6.8 kg] | 11” [ 280 mm] | 9.2” [ 230 mm] | 4.3” [110 mm] |
| C60 | 6,000 lbs [2700 kg] | 16.5lb [6.8 kg] | 11.3”[290 mm] | 9.2” [230 mm ] | 4.3” [110 mm] |

- Cages have been designed to accept SWA-6 swivel and/or SA-P-6 Shock absorber.

- Universal Joint is available. Replaces shackle and eliminates cutting long line.

CANAM’s Cargo Hooks are precision engineered from high quality materials for maximum strength and endurance.

Each unit is proof tested prior to release.

Certificate available upon request.

Hook with wrap around cage

Ringed cage also available