# Product Features

## Key Characteristics

- Full PCS band support in 5, 10, or 15 MHz steps

- Industry leading RF output power; 43dBm(20W) Down Link and 30dBm(1W) Up Link

- Diversity Configuration provides Superior Up Link Performance

- Supports IS95 and CDMA2000 systems

- Ubiquitous compatibility with multi-vendor BTS equipment

- Automatic Loop Back Detect provides simplified site specific optimization

- Flexible system configuration via PC based NMS application or local Keyboard

- Sophisticated Alarm and Monitoring functionality via wireless or wired modem

- Wireless Modem and NMS application allows Laptop equipped Technicians to access the Repeater without visiting the repeater or the central OMC

- Integrated OMC connectivity via standards based SNMP

- Intelligent Automatic Gain Control and Temperature Compensation Algorithms

- User defined Temperature Threshold Alarm

- RF Monitoring Ports for Interference Analysis without interrupting service

- Flexible equipment placement (Indoor or Outdoor)

- Secure Keyed Door Lock

- Integrated RF lightning protection

- Integrated Battery Revert and Charging

- Reliable Fanless Cooling System

## Front View

Figure 1 Front View

Front Panel LEDs : See Section 1.4

## Bottom View

Figure 2 Bottom View

BATTERY:			Battery Connection Port (+24V)

DIV-ANT:				Reverse Diversity Link Input Port (N-Type Female)

DIV-MON:			Reverse Diversity Link Monitoring Port (-30 dB, N-Type Female)

SERVICE-ANT: 	Reverse Link Input / Forward Link Output Port (N-Type Female)

SERVICE-MON: 	Forward Link Output Monitoring Port (-30dB, N-Type Female)

MODEM-ANT:		CDMA Modem Antenna Port (SMA Female)

DONOR-OUT: 		Forward Link Input / Reverse Link Output Port(N-Type Female)

DONOR-MON: 	Reverse Link Output Monitoring Port (-30dB, N-Type Female)

PSTN:					PSTN Dial-up Modem Connection Port (9 Pin D sub)

POWER : 				Power Source (110V ~ 220V/AC )

## Front Panel LED Display

Figure 3 Front Panel LED

There are three LEDs on the front panel for instant fault detection at the site. A detailed description of each LED is as follows.

- POWER: This LED shows the external AC or internal DC status of the repeater.

Normal:		Green LED on

Abnormal:	LED off

- RUN : This LED shows the status of the repeater’s internal control board.

Normal:		Green LED blinks every second

###### Abnormal:	Green LED off if control board malfunctions.

- ALM : This LED shows the status of the monitored alarms.

Normal:		Red LED off

###### Abnormal:	Red LED on

# Specifications

## RF Specifications

- Input/Output Frequency Range

- Forward Link Direction:		1930~1990MHz

(Input port: from BTS, Output Port: to Mobile Station)

- Reverse Link Direction:		1850 ~ 1910MHz

(Input Port: from Mobile Station, Output Port: to BTS)

- Bandwidth:								5MHz, 10MHz, or 15 MHz (Option)

- Input Level

- Forward Link: 					-52 ~ -32dBm/Total

- Reverse Link: 						-119 ~ -55dBm/Total

- Maximum input level:				+ 10dBm

- Gain Control Range, Step and Accuracy

- Forward Link Direction:		65 ~ 95dB, 1dB Step

- Reverse Link Direction: 		60 ~ 90dB, 1dB Step

- Attenuation Accuracy : 			±1dB@0dB~20dB, ±1.5dB@21dB~30dB

- AGC :									> 10dB (not over Max Power ±2.0dB)

- Pass Band Flatness:					3dBp-p, max @CW Test

- RF Output Level

- Forward Link Output: 		43dBm(20W) Total

- Reverse Link Output: 		30dBm(1W) Total

- Channel Bandwidth: 				1.25 MHz

- Protocol Support:					IS95, CDMA2000

- Forward Link Spurious Emissions:

- Fc (885KHz:			 		-45dBc (min) @ 30KHz RBW

- Fc (1.98MHz:		 			-55dBc (min) @ 30KHz RBW

- Reverse Link Spurious Emissions:

- Fc (885KHz:			 		-45dBc (min) @ 30KHz RBW

- Fc (1.98MHz:		 			-55dBc (min) @ 30KHz RBW

- Noise Figure	(FWD, RVS Single):	< 4dB

(RVS Main + Div):		< 6dB

- Propagation Delay: 					< 5 ㎲

- In/Out VSWR: 						< 1.5:1

- Waveform Quality (FWD) 		> 0.950 @ full nominal rated power

- Waveform Quality (RVS) 			> 0.960 @ full nominal rated power

- Over VSWR Protection

- Over Temperature Protection (Shutdown and Restart)

- Frequency Stability :					< 0.05ppm

- In Band Spurious(>±2.25MHz):	< -13dBm/1MHz

- Out of Band Spurious :				< -36dBm/1kHz @ 9kHz~150kHz,

< -36dBm/10kHz @ 150kHz~30MHz

< -36dBm/100kHz @ 30MHz~1GHz

< -30dBm/1MHz @ 1GHz~12.56GHz														< -47dBm/100kHz @ 806MHz~849MHz

< -47dBm/100kHz @ 869MHz~960MHz

< -47dBm/100kHz @ 3.4GHz~3.53GHz

(ANSI J-STD-008 Compliant)

## Controller Interface

- Control Method

- Dedicated PC with OMC Software

- ASYNC, Full Duplex

- Protocol: HDLC, 57600bps

- Local Connection: 		RS232C

- PSTN Connection:		Modem

- Wireless Connection:	1XRTT Modem

- Custom Configured SNMP Interface

- User Controlled Parameters

- Repeater ID

- Repeater Type

- Version

- Over Temperature Threshold Level

- Forward / Reverse HPA On/Off

- Forward / Reverse AGC On/Off

- Forward / Reverse Temperature Compensation On/Off

- Forward / Reverse AGC Level

- Forward / Reverse Over Power Level

- Forward / Reverse Attenuation Value

- Forward / Reverse Band Selection

- Alarm and Status Display Items

- Repeater ID

- Current ambient Temperature

- Over Temperature threshold Level

- Forward / Reverse Current Output Power Level

- Forward / Reverse Attenuation Level

- Forward / Reverse current Gain

- Forward / Reverse HPA Power On/Off Status

- Forward / Reverse AGC On/Off Status

- Forward / Reverse AGC Level

- Forward / Reverse Over Power Level

- Forward / Reverse Frequency Band

- Forward / Reverse Frequency Lock Fail Alarm

- Forward / Reverse Over Power Alarm (based on the setting value)

- Forward / Reverse HPA VSWR Alarm

- Forward / Reverse HPA Over Temperature Alarm

- Forward / Reverse HPA Over Power Alarm

- Power Supply AC / DC / Battery Fail Alarm

- Door Open Alarm

- Record Alarm History (contents, date)

## Mechanical Specifications

- Size:											28.94”(H) × 17.95”(W) × 10.63”(D)

- Net Weight: 								99.2 lbs.

- Connectors

- Input / Output ANT Port:			N Type – female

- Monitoring Port:						N Type – female

- Frame Ground:						Hex Nut (6M)

- RS232C:								9Pin D-SUB, Female (on MCU Panel)

- Door Lock:								Key

- Heat Dissipation: 						Natural Conduction

- Housing Class:							IP55

## Electrical Specifications

- Main AC Input:						   	110 ~ 220V AC

- DC Output:								27V, 9V

- Power Consumption: 					350W Maximum

- Battery Back-up: 	Automatic Sensing, Switchover, and Charge to
External Battery (Available w/ Optional Battery Backup)

## Environmental Specifications

- Operating Temperature: 				-30℃ ~ +55℃

- Humidity:									95%, Relative

## Warranty

- 3 Year Limited Warranty

# Text boxes

# 20Watt CDMA RF Repeater System