LOBO RAISED PANEL, LINE COPY SHAPER

CS-40PAME 40” MENU COPY SHAER

CS-55PAME 55” MENU COPY SHAPER

CS-40PAAU 40” AUTO COPY SHAPER

CS-55PAAU 55” AUTO COPY SHAPER

*Those model are special design to make all the parts for raised panel doors by one spindle shaper without change knife (rail, stile, panel) to get mass production.

*Also enable to do the chair leg, furniture parts by the 7” in and out copy capacity.

*4” high stackable spindle with pneumatic stop for easy and accuracy setup for each cutter position.

*Rigid construction made by heavy sheet metal frame, case iron table & base

*Table move from right to left by hydraulic to achieve fully cutting power.

*Table move in and out, follow by the template, control by the pneumatic pressure to ensure the same shape was copy.

*Limit switch to control cutting cycle for fast production and time saving.

*Liner guides & rails for smooth movement and long life usage.

*Strong cutting power.  Do not need to be precut for the arch or oval panel.

*Cast iron fence located in the squire groove to finish square cut easily.

Specification                                CS-40PAME(AU)        CS-55PAME(AU)

Max. Cutting Capacity

Length (left to right)                         40”                                  55”

Width (in and out)                              7”                                    7”

Thickness

Max. Cutter Size

Spindle Diameter                                 1-1/4”                              1-1/4”

Spindle Length

Spindle speed

Main Motor                                             7-1/2HP

Hyd. Pump

Dust Hood                                                  4”                             4”

Net Weight                                              2090 LBS

Gross Weight                                           2530 LBS

PNEUMATIC FENCE &                             CONTROL PANEL                        TEMPLATE

STACKABLE SPINDLE