MODEL 2000R 18

Radar Speed Monitor

Trailer Dimensions:

Length with tongue		128"

Length without tongue		80"

Width with fenders		72"

Top of sign panel raised		129"

Bottom of sign speed monitor	62"

Speed monitor-housing		34" x 34"

Trailer Specifications:

Frame and Deck			2" x 2" x 1/8" tubular steel—1/8 Diamond plate steel deck.

Axle and Springs	Straight tubular steel axle with capacity of 2000 LB— Minimum three leaf 1000 LB

Wheels and Tires			Five lug—P205/75R15

Fenders				16 gauge steel, walkable

Tongue and Safety chains		2" hitch— Two chains with 1/4" minimum diameter safety hooks.

Jacks	Four adjustable 2000-LB capacity, each corner.

Tail lights	Dual combination reflective light with stop, tail, and turn signal. Male and female quick connect. License plate bracket.

Wiring	Wiring to be enclosed in jacketed cable or conduit

Lift wench	Gear ration-4:1, Load Capacity-1200 LBS./544 KG, Reel Capacity 7/32" dia. Cable, 58 FT.

Battery/controller box	Steel fabrication, double lockable, hinged, ventilated and mounted on a trailer deck, to protect batteries, control module and instrument panel from the weather and vandalism.

Display and Radar Detection

Speed ranges from 5-99mph with 1000-ft. visibility. Speed sign -20" two digits. Red LED sign and antenna; two digit. One tuning fork with case (specify speed). A weatherproof metal casing encloses a display of module, electronics, and radar, and is able to withstand the harsh outdoor environments.

1/4 to1/2 mile and 3" Head Diameter K Band

Solar and Charging

Autonomy			Unit will operate for 30 days without the aid of the solar panels

Battery bank			Six 12-volt batteries wired for 660 amps operation

Electronic circuitry	Solid State, reverse polarity protection, properly fused, disconnects on all cables.

Battery Charger	The 120 volt/10 amp charger will automatically shut down when the batteries are fully charged.

Solar Panel

Typical Electrical Characteristics		75 Watt

Peak Power (Wp)			Watts 	75

Open Circuit Voltage (Voc)	Volts	21.0

Max. Power Voltage (Vmp)	Volts	17.0

Short Circuit Current (Isc)		Amps	4.8

Max. Power Current (Imp)		Amps	4.4

Short Circuit Temp. Coefficient	mA/°C	+3.0

Open Circuit Voltage Coefficient	V/°C	-0.09

Max. Series Fuse			Amps	10

Solid State Regulator

Electrical Specifications			SRX-6/12

Nominal system V			12V

Maximum input current			5.5A

Input V range				15V-25V

Shunting V @ 25 degrees C		14.6 t 0.2V

Options

Time clock, battery cabinet alarm, double 8" flashers, overspeed violation flashing indication, siren or strobe light, spare wheel, tire and mount, 80-watt solar panel, 120-watt solar panel.

Manufacturer reserves the right to make changes in its products from time to time without incurring any obligation to incorporate such improvements in any products previously sold or in service.